## Slide 1
SuPeRBE Training Material
Climate change and built environment
Fundamentals of climate change
Level of competence: 2
Activity 3.2
SuPeRBE Project (CE0200768)
SuPeRBE Training Material
Level of competence: 1/2/3
Area of Expertise: AD2.3 according
to the CEN Workshop Agreement 17939
AD2 RBE Assessment System - RNTool - RBTool
AD2.3 RNTool-CE
Macro Area of Expertise:
Area of Expertise:

## Slide 2
The Resilient Neighbourhood Tool (RNTool) is the generic framework that implements the RBE Method at the neighbourhood scale. It translates the methodological structure of the RBE Method into a tool capable of assessing the overall level of climate risk across hazards, urban sectors, and exposed elements.
What is the RNTool?
Key points RNTool
-Modular and adaptable structure.
-7 Hazards, 84 Risk Categories, >1000 assessment criteria.
-Goal: provide cities with a customisable and operational tool for climate adaptation.
2

## Slide 3
The RNTool Central European version supports climate risk assessment in relation to the following 7 Issues:
Structure of RNTool
B Floods
C Extreme heat
D Droughts
E Storms
F Wild-fire
G Mass Movement
A Heavy precipitation
ISSUES
3

## Slide 4
Representing key Urban Sectors (8), addressed in RNTool for Central Europe are:
Structure of RNTool
Tourism (Heavy precipitation, Extreme Heat, Mass Movement)
Emergency Services (Heavy precipitation, Floods, Extreme Heat, Drought, Storms, Wild-Fire, Mass Movement)
Health (Heavy precipitation, Floods, Extreme Heat, Drought, Storms)
Environment and Biodiversity (Extreme Heat, Drought)
Water (Floods, Drought)
Energy (Heavy precipitation, Extreme Heat, Storms)
Transport (Heavy precipitation, Floods, Extreme Heat, Storms, Wild-fire, Mass Movement)
Buildings (Heavy precipitation, Floods, Extreme Heat, Storms, Mass Movement)
Macro categories
4

## Slide 5
A Risk Category represents the specific risk arising from the interaction between a Hazard (Issue) and an Exposed Element within a particular Urban Sector (Macro Category).
Structure of RNTool
Risk categories
84 Risk Categories have been defined in the Central European version of the RNTool. These categories cover all seven Issues (Hazards) addressed in the tool and span across the key Urban Sectors most relevant for neighbourhood-scale climate adaptation.
Hazard: Heavy precipitation
Urban sector:
Water
Exposed element: Impervious Surface Coverage
Category: A4.2 Damage risk Water supply network
Represents the interaction between
within a particular
5

## Slide 6
6

## Slide 7
7

## Slide 8
The number of vulnerability and exposure criteria per Hazard (Issue) is:
Heavy Precipitation: 240
Floods: 300
Extreme Heat: 157
Droughts: 36
Storms: 124
Wildfire: 15
Mass Movement: 80
Each Risk Category in the RNTool is assessed through a structured set of criteria, which are operationalised via indicators. These indicators serve as the fundamental units for measuring the level of vulnerability, exposure, and hazard at the neighbourhood scale.
Structure of RNTool
Criteria and indicators
The RNTool Central European version includes a total of 1,022 assessment criteria, distributed as follows:
952 vulnerability and exposure criteria (directly associated with Risk Categories)
70 hazard criteria (associated with the Issues).
8

## Slide 9
Structure of RNTool
Criteria and indicators examples
G10 | TOURISM |  | 
G10.1 | Damage risk for hotels and resorts |  | 
VULNERABILITY |  |  | 
Code | Criterion | Indicator | Unit
G10.1.1 | Slope crest or toe | Distance from Slope Crest or Toe | Meters (m)
G10.1.2 | Drainage Systems on Site | Presence of drainage system within the area | Capacity in liters per second (L/s); Condition (Good/Fair/Poor)
G10.1.3 | Retaining Structures | Presence of Retaining Structures or Slope Stabilization Systems | (Yes/No)
EXPOSURE |  |  | 
G10.1-E1 | Hotels and resorts density | Total built volume of hotels and resorts divided by the extension of the urban area | m3/m2
9

## Slide 10
Structure of RNTool
6
References: scientific literature, technical standards, or institutional sources that validate the indicator.
5
Data sources, suggestions on where to find or how to collect the data required
4
The assessment method, a guideline on how the indicator value should be calculated or determined
3
Benchmark values:
benchmark 0, optimal condition (normalized score = 0)
benchmark 1, critical condition (normalized score = 1)
2
Direction of performance: Higher is Better (HiB), Lower is Better (LiB), or Qualitative
1
Description of the indicator and its unit of measure (if applicable)
For each indicator, the RNTool provides:
Note: Benchmarks are defined in the RNTool but are intended to be adapted to local contexts for effective use.
10

## Slide 11
Contextualisation of RNTool
The RNTool is a generic assessment framework, providing a comprehensive structure for evaluating climate risks at the neighbourhood scale.
However, to become an operational tool the RNTool must undergo a contextualisation process. This process transforms the generic framework into an operational assessment tool.
The contextualisation process includes several key steps, each of which contributes to tailoring the RNTool to the unique characteristics of the local context.
11
Key Steps:
Selection of Relevant Issues (Hazards)
Selection of Macro-Categories (Urban Sectors)
Selection of Risk Categories
Benchmarking of criterio
Assignment of Weights

## Slide 12
To become an operational tool the RNTool must undergo a contextualisation process. This process transforms the generic framework into an operational assessment tool. The contextualisation process includes several key steps, each of which contributes to tailoring the RNTool to the unique characteristics of the local context.
Contextualisation of RNTool
First step: The selection of relevant Issues (Hazards) most pertinent to the specific context of the municipality. This selection can be guided by:
5.2.1 Selection of Relevant Issues (Hazards)
Consultation with local experts and stakeholders.
Historical data on extreme weather events
Regional or national climate adaptation plans and strategies
Existing SECAPs (Sustainable Energy and Climate Action Plans)
12

## Slide 13
Contextualisation of RNTool
Second step:
For each selected Issue (Hazard), the next step is to identify the Urban Sectors (Macro-Categories) that are exposed and potentially affected. This selection is based on:
5.2.2 Selection of Macro-Categories (Urban Sectors)
The institutional capacity to implement adaptation measures within each sector.
The dependency of services on exposed infrastructure. If the proper functioning of a sector (e.g., Health) relies on infrastructure that is at risk from a certain hazard, then that infrastructure’s sector (e.g., Energy, Water, Mobility) should be included in the assessment even if it’s not the primary target of the hazard.
The presence and criticality of urban functions in the municipality (e.g., Mobility, Health, Water)
13

## Slide 14
Contextualisation of RNTool
Third step:
Once the relevant Urban Sectors are selected, the next step is to determine the Risk Categories representing the specific interactions between hazards and exposed elements that represent tangible and assessable climate risks. Only the most relevant and assessable Risk Categories should be retained, based on:
5.2.3 Selection of risk categories
Stakeholder priorities
Strategic relevance for local planning
Availability of data
14

## Slide 15
Contextualisation of RNTool
Fourth step:
Each Risk Category is assessed through a set of criteria (hazard, exposure, and vulnerability), each linked to a specific indicator. The contextualisation process requires:
5.2.4 Benchmarking of criteria
Defining or adapting the assessment method for calculating the indicator value.
Assigning local benchmarks (value 0 for optimal performance and value 1 for critical performance)
When localising benchmarks and methods, the following hierarchy of sources should be respected:
Binding regulations (e.g., building codes, laws)
Recognised technical standards (e.g., ISO, CEN, national standards)
Authoritative guidelines (e.g., national planning documents, EU reports)
Peer-reviewed scientific literature and other technical references.
1
2
3
4
15

## Slide 16
Contextualisation of RNTool
Fifth step:
Assignment of weights at multiple levels of the risk calculation process. Weights influence the relative importance of different criteria and risk components, affecting how final risk values are calculated and interpreted. To ensure transparency, consistency, and relevance, the following general principles should be followed when assigning weights in the RNTool:
5.2.5 Assignment of Weights
Transparent: The rationale for each weight must be documented to allow future updates or audits.
Participatory. Weights should ideally be defined through consultation with local experts, stakeholders, and cross-sectoral teams (e.g. urban planners, emergency services, environmental agencies).
Purpose driven. Weights should reflect local policy priorities, the perceived severity of impacts, and the reliability of available data.
16

## Slide 17
Assessment Outputs of RNTool
Risk values provided for
Applications
Overall Risk
Hazards
Urban Sectors
Categories
Integrated urban strategies
EU or national funding (e.g., PNRR)
Adaptation plans
17

## Slide 18
Practical Example of RNTool
Step 1 Assignment of Hazard Values to Issues
1.1 The value of likelihood of Hazard is assigned (HV)
Code | Hazard | HV
A | Heavy Precipitation | 0,8
C | Extreme Temperatures | 0,9
HV value ranges from 0 to 1. HV answers the question: how severe is the hazard ?
Option 1
18

## Slide 19
Practical Example of RNTool
In alternative, climatic indicators can be used to determine HV. The following is an example for Hazard A Heavy Precipitation
Code | Hazard criteria | Hazard indicator | Unit of measure | Value
H.A1 | R20 | Number of Days with Precipitation ≥ 20 mm | number | 2
H.A2 | SDII | Simple Daily Intensity Index | mm/day | 8
H.A3 | RX1DAY | Maximum total precipitation that falls in a single day | mm | 60
Step 1
Option 2
19

## Slide 20
Practical Example of RNTool
The value of climatic hazards is normalised in the interval (0-1) - Example for H.A3
Code | Hazard criteria | Hazard indicator | Unit of measure | Value
H.A3 | RX1DAY | Maximum total precipitation that falls in a single day | mm | 60
Benchmark 1 - Critical | Xmax | 100
Benchmark 0- Optimal | Xmin | 20
Value of the indicator | Xi | 60
Normalised Value |  | 0,5
Type: Lower is better
Nv = Xi - Xmin
Xmax - Xmin
Step 1
Option 2
20

## Slide 21
Practical Example of RNTool
The value of climatic hazards is normalised in the interval (0-1) - Example for H.A3
Code | Hazard criteria | Hazard indicator | Normalised Value | Weight | Weighted value
H.A1 | R20 | Number of Days with Precipitation ≥ 20 mm | 0,7 | 0,33 | 0,23
H.A2 | SDII | Simple Daily Intensity Index | 0,7 | 0,33 | 0,23
H.A3 | RX1DAY | Maximum total precipitation that falls in a single day | 0,5 | 0,33 | 0,17
HV: 0,63
Note: Weighted value = normalised value * weight
Step 1
Option 2
21

## Slide 22
Practical Example of RNTool
Step 2 Exposure Value (EV) calculation for Risk Categories
The value of the Exposure Indicators associated with Risk Categories is calculated
A | Heavy Precipitation |  |  |  |  | 
A2 | Transports | Exposure Criteria |  | Exposure Indicator | Unit | Value
A2.1 | Damage risk for public transit infrastructure | E.A2.1 | Public transport density | Total length of public transport routes per unit area of the urban area. | km/km² | 2
A2.3 | Damage risk for bicycle and pedestrian paths | E.A2.3 | Extention of bicycle and pedestrian paths | Meters of bicycle and pedestrian paths per inhabitant | m/inhabitant | 0,8
A2.4 | Damage risk for road network | E.A2.4 | Road density | Total road length divided by the urban area. | km/km² | 2,8
A3 | Energy | Exposure Criteria |  | Exposure Indicator | Unit | Value
A3.1 | Damage Risk for Power Lines | E.A3.1 | Exposed power lines | Share of exposed power lines | % | 90
22

## Slide 23
Practical Example of RNTool
Step 2
The value of the Exposure Indicators associated with Risk Categories is calculated
C | Extreme Heat |  |  |  |  | 
C3 | Energy | Exposure Criteria |  | Exposure Indicator | Unit | Value
C3.1 | Damage risk for Electrical Grid Infrastructure | E.C3.1 | Grid Density | Total length of transmission and distribution lines per unit area. | km/km² | 5,2
C3.2 | Damage risk for Renewable Energy Installations (PV) | E.C3.2 | Photovoltaic power density | Photovoltaic power density per unit area | kWp/km2 | 50
C8 | Health | Exposure Criteria |  | Exposure Indicator | Unit | Value
C8.1 | Health risk for inhabitants | E.C8.1 | Population density | total number of inhabitants divided by the total area of the urban zone | n/km2 | 6590
23

## Slide 24
Practical Example of RNTool
The value of the Exposure Indicators is normalised in the interval 0-1 to calculate the Exposure Value (EV)
C8 | Health | Exposure criterion | Exposure indicator | Unit | Value
C8.1 | Health risk for inhabitants | Population density | total number of inhabitants divided by the total area of the urban zone | n/km2 | 6590
Benchmark 1 - Critical | Xmax | 10000
Benchmark 0- Optimal | Xmin | 1000
Value of the indicator | Xi | 6590
Normalised Value |  | 0,6
Type: Lower is better
Nv = Xi - Xmin
Xmax - Xmin
Step 2
24

## Slide 25
Practical Example of RNTool
Table with the Exposure Values calculated for all Risk Categories
A | Heavy precipitation | 
A2 | Transports | EV
A2.1 | Damage risk for public transit infrastructure | 0,8
A2.3 | Damage risk for bicycle and pedestrian paths | 0,6
A2.4 | Damage risk for road network | 0,7
A3 | Energy | EV
A3.1 | Damage Risk for Power Lines | 0,8
Step 2
25

## Slide 26
Practical Example of RNTool
Table with the Exposure Values calculated for all Risk Categories
C | Extreme temperatures | 
C3 | Energy | EV
C3.1 | Damage risk for Electrical Grid Infrastructure | 0,9
C3.2 | Damage risk for Renewable Energy Installations | 0,7
C8 | Health | EV
C8.1 | Health risk for inhabitants | 0,6
Step 2
26

## Slide 27
Practical Example of RNTool
The value of the Vulnerability Indicators of Risk Categories is calculated (example for the Risk Category C8.1)
Step 3/4/5 Vulnerability Values calculation for Risk Categories
C8.1 Health risk for inhabitants |  | Code | Criterion | Indicator | Unit | Value
 |  | C8.1.1 | Capacity of paved surfaces to reflect solar radiation | mean SRI | n | 16
 |  | C8.1.2 | Capacity of roofs to reflect solar radiation | mean SRI | n | 37
 |  | C8.1.3 | Urban Area Reflectivity | mean albedo | n | 0,27
 |  | C8.1.4 | Shading of paved surfaces | Share of shaded paved areas | % | 20
 |  | C8.1.5 | Visibility of the Sky | mean Sky View Factor | n | 0,74
 |  | C8.1.6 | Availability of green areas | Share of green areas of total urban zone area | % | 19
27

## Slide 28
Practical Example of RNTool
The value of the Vulnerability Indicators of Risk Categories is normalised in the interval 0-1 (Example for criterion C8.1.1)
Step 3/4/5 Vulnerability Values calculation for Risk Categories
Criterion | Indicator | Unit | Value
Capacity of paved surfaces to reflect solar radiation | mean SRI | n | 16
Benchmark 1 - Critical | Xmax | 58
Benchmark 0- Optimal | Xmin | 0
Value of the indicator | Xi | 16
Normalised Value |  | 0,7
Type: Higher is better
Nv = Xi - Xmin
Xmax - Xmin
28

## Slide 29
Practical Example of RNTool
To calculate the Vulnerability Value (VV) for Risk Categories a weight shall be assigned to Vulnerability Indicators (Example for Risk Category C8)
Step 3/4/5 Vulnerability Values calculation for Risk Categories
C8.1 Health risk for inhabitants |  | Code | Criterion | Normalised value
 |  | C8.1.1 | Capacity of paved surfaces to reflect solar radiation | 0,7
 |  | C8.1.2 | Capacity of roofs to reflect solar radiation | 0,36
 |  | C8.1.3 | Urban Area Reflectivity | 0,66
 |  | C8.1.4 | Shading of paved surfaces | 0,6
 |  | C8.1.5 | Visibility of the Sky | 0,26
 |  | C8.1.6 | Availability of green areas | 0,74
29

## Slide 30
Practical Example of RNTool
The value of the Vulnerability Indicators of Risk Categories is calculated (example for the Risk Category C8.1)
Step 3/4/5 Vulnerability Values calculation for Risk Categories
C8.1 Health risk for inhabitants |  | Code | Criterion | Normalised value | Weight
 |  | C8.1.1 | Capacity of paved surfaces to reflect solar radiation | 0,7 | 0,25
 |  | C8.1.2 | Capacity of roofs to reflect solar radiation | 0,36 | 0,15
 |  | C8.1.3 | Urban Area Reflectivity | 0,66 | 0,2
 |  | C8.1.4 | Shading of paved surfaces | 0,6 | 0,1
 |  | C8.1.5 | Visibility of the Sky | 0,26 | 0,1
 |  | C8.1.6 | Availability of green areas | 0,74 | 0,2
30

## Slide 31
Practical Example of RNTool
The value of the Vulnerability Indicators of Risk Categories is calculated (example for the Risk Category C8.1)
Step 3/4/5 Vulnerability Values calculation for Risk Categories
C8.1 Health risk for inhabitants |  | Code | Criterion | Normalised value | Weight | Weight value
 |  | C8.1.1 | Capacity of paved surfaces to reflect solar radiation | 0,7 | 0,25 | 0,2
 |  | C8.1.2 | Capacity of roofs to reflect solar radiation | 0,36 | 0,15 | 0,1
 |  | C8.1.3 | Urban Area Reflectivity | 0,66 | 0,2 | 0,1
 |  | C8.1.4 | Shading of paved surfaces | 0,6 | 0,1 | 0,1
 |  | C8.1.5 | Visibility of the Sky | 0,26 | 0,1 | 0,02
 |  | C8.1.6 | Availability of green areas | 0,74 | 0,2 | 0,1
0,6
31

## Slide 32
Practical Example of RNTool
Risk Value of Risk Categories is calculated as a weighted geometrical mean of HV, EV and VV (Example for Risk Category C8)
Step 6 Calculation of the Risk Value for Risk Categories
C8 | Health | Weight
Hazard (HV) | 0,9 | 0,25
Exposure (EV) | 0,6 | 0,25
Vulnerability (VV) | 0,6 | 0,5
Category risk value |  | 0,67
Note: Weights are assigned by the user, Total value must be 1
32

## Slide 33
Practical Example of RNTool
Risk Value of Macro Categories is calculated as a weighted sum of Risk Values of the Categories
Step 7 Calculation of Risk Value for the Urban Sector (Macro-Category)
A2 | Transports | Category risk level | Weight | Weighted value
A2.1 | Damage risk for public transit infrastructure | 0,67 | 0,5 | 0,3
A2.3 | Damage risk for bicycle and pedestrian paths | 0,82 | 0,25 | 0,2
A2.4 | Damage risk for road network | 0,65 | 0,25 | 0,2
Macro category risk value |  |  |  | 0,7
Note: Weights are assigned by the user, Total value must be 1
33

## Slide 34
Practical Example of RNTool
Risk Value in relation to the Hazard calculated as a weighted sum of Risk Values of the Macro Categories (Example for Hazard A)
Step 8 Calculation of Risk Value for a Hazard
A | Heavy precipitation | Macro category risk level | Weight | Weighted value
A2 | Transports | 0,70 | 0,5 | 0,35
A3 | Energy | 0,82 | 0,5 | 0,41
Hazard risk value |  |  |  | 0,76
Note: Weights are assigned by the user, Total value must be 1
34

## Slide 35
Practical Example of RNTool
Overall Risk Value calculated as a weighted sum of Risk Values of Hazards
Step 9 Calculation of overall Risk Value
Code | Hazard | Hazard risk value | Weight | Weighted value
A | Heavy precipitation | 0,76 | 0,4 | 0,3
C | Extreme temperatures | 0,82 | 0,6 | 0,5
Overall risk value |  |  |  | 0,8
Note: Weights are assigned by the user, Total value must be 1
35

## Slide 36
RISK ASSESSMENT RESULTS BY CATEGORY
The rating system also produces results at the level of the Exposed Elements within an Urban Sector.
Damage risk for public transit infrastructure
Damage risk for bicycle and pedestrian paths
RISK 0,67
36
Risk Category
Urban sector: Transport
Damage risk for road network
RISK 0,82
RISK 0,65

## Slide 37
RISK ASSESSMENT RESULTS BY URBAN SECTOR
For each climate hazard, the rating system produces a score that indicates the risk level of the urban sectors included in the assessment.
Hazard: Heavy precipitation
Transports
Energy
RISK 0,70
RISK 0,82
37
Urban Sectors

## Slide 38
RISK ASSESSMENT RESULTS BY HAZARD AND OVERALL
The application of the assessment system produces scores (0,1) that represent:
the overall risk level of the urban area
the risk associated with each individual hazard
the risk by Urban Sector
the risk concerning specific exposed elements
OVERALL RISK – 0,80
RISK PER HAZARD
Extreme Temperatures
Heavy Precipitation
RISK 0,76
RISK 0,82
38