## Slide 1
SuPeRBE Training Material
Climate change and built environment
Fundamentals of climate change
Level of competence: 2
Activity 3.2
SuPeRBE Project (CE0200768)
SuPeRBE Training Material
Area of Expertise: 6.2 according
to the CEN Workshop Agreement 17939
Level of competence: 1/2/3
Macro Area of Expertise 6:
Risk Assessment At Small Urban Scale
Hazard: Drought (D)
Risk Category: Damage Risk for Urban Green Spaces (D7.1) & Damage Risk for Street Trees (D7.2)
Urban Sector: Environment & biodiversity (D7)
Area of Expertise 6.1:

## Slide 2: DROUGHT
“A period of abnormally dry weather long enough to cause a serious hydrological imbalance.” (source: https://www.ipcc.ch/sr15/chapter/glossary/)
Natural phenomenon
Intensified in recent decades by climate change and unsustainable land practices
Human-induced climate change has contributed to increases in droughts due to increased atmospheric evaporative demand induced by increased temperature, decreased relative humidity, and increased net radiation
More regions are affected by drought with increasing global warming
General Information
Notes: - Megadrought – “A megadrought is a very lengthy and pervasive drought, lasting much longer than normal, usually a decade or more” (https://www.ipcc.ch/sr15/chapter/glossary/))
Number of droughts has surged by nearly 30 per cent in frequency and intensity since 2000
result of a complicated set of events driven or amplified by climate change, as well as sometimes the mismanagement of land (For example, a hillside which is deforested is immediately degraded. The land will lose its resilience to extreme weather and will become more susceptible to both drought and flooding.)
WHO: An estimated 55 million people globally are affected by droughts every year, and they are the most serious hazard to livestock and crops in nearly every part of the world. Drought threatens people’s livelihoods, increases the risk of disease and death, and fuels mass migration. Water scarcity impacts 40% of the world’s population, and as many as 700 million people are at-risk of being displaced as a result of drought by 2030
Additional info:
https://news.un.org/en/story/2024/12/1157696
https://www.ipcc.ch/report/ar6/wg1/chapter/chapter-11/
https://www.who.int/health-topics/drought/#tab=tab_1

## Slide 3: TYPES OF DROUGHT
Net water availability – caused by precipitation deficits and changes in evapotranspiration
Agricultural drought – caused by a lack of sufficient soil moisture and increased atmospheric evaporative demand
Ecological drought - caused by a lack of sufficient soil moisture and increased atmospheric evaporative demand
Hydrological drought – caused by a lack of runoff and surface water

## Slide 4
Water supply system
  Damage risk for water treatment plants
  Damage risk for the water supply network
Environment & biodiversity
  Damage risk for urban green spaces
  Damage risk for street trees
Health
  Health risk for the population
Emergency services
  Efficiency risk for the fire brigade
  Efficiency risk for emergency medical services
AFFECTED URBAN SYSTEMS

## Slide 5
Hazard: Drought
Exposed element: Urban green spaces
RISK ASSESSMENT FOR DAMAGE RISK FOR URBAN GREEN SPACES
DROUGHT
DAMAGE RISK FOR URBAN GREEN SPACES
URBAN GREEN SPACES
HAZARD
EXPOSED ELEMENT
RISK CATEGORY

## Slide 6
IMPACT CHAIN
HAZARD
DROUGHT
DAMAGE RISK FOR URBAN GREEN SPACES
EXPOSED ELEMENT
RISK CATEGORY
RISK ASSESSMENT RESULT
URBAN GREEN SPACES
VULNERABILITY
Sensitivity
Adaptive capacity

## Slide 7
Soil stress
Endangered species
Habitats at risk
Areas at risk
Protected urban green spaces
VULNERABILITY CRITERIA
HAZARD
DROUGHT
DAMAGE RISK FOR URBAN GREEN SPACES
EXPOSED ELEMENT
RISK CATEGORY
RISK ASSESSMENT RESULT
URBAN GREEN SPACES
VULNERABILITY
Sensitivity
Adaptive capacity

## Slide 8
CRITERION | INDICATOR
Soil stress | Soil moisture stress
Endangered species | Number of endangered species
Habitats at risk | Percentage of vulnerable habitats
Areas at risk | Percentage of protected areas
Protected urban green spaces | Percentage of watered urban green spaces
VULNERABILITY ASSESSMENT
HAZARD
DROUGHT
DAMAGE RISK FOR URBAN GREEN SPACES
EXPOSED ELEMENT
RISK CATEGORY
RISK ASSESSMENT RESULT
URBAN GREEN SPACES
VULNERABILITY
Sensitivity
Adaptive capacity

## Slide 9
NORMALISATION INTERVAL
Normalisation
Normalization is a crucial step in this process, as it transforms diverse indicator values into a common scale, typically ranging from 0 to 1. This ensures that each indicator contributes proportionately and comparably to the overall resilience score, regardless of its original unit or magnitude. By applying normalization, we enable meaningful synthesis of data, facilitate benchmarking across different contexts, and support more transparent and objective decision-making in resilience evaluations.

## Slide 10
Description:
Number of days in a year on which soil moisture levels are not sufficient to meet the vegetation water demand (based on the requirements of plant species by land use type and the amount of water available in the soil)
Objective:
To quantify soil water deficit as an early indicator of drought, to assess ecosystem and vegetation vulnerability, and to integrate hydro-climatic and land-surface data.
Relevance:
Declining soil moisture is often the first indicator of drought conditions. Soil moisture stress reduces vegetation cover and evapotranspiration, and persistent dryness affects ecosystem stability.
D7.1.1 SOIL MOISTURE STRESS

## Slide 11
Find the data for your area at: https://european-crt.org/map.html or the national database
CALCULATION: STEP-BY-STEP EXAMPLE
D7.1.1 SOIL MOISTURE STRESS

## Slide 12
Critical value (1) = National average +20%
Optimal value (0) = National average -20%
Range of values: higher is better (HIB)
D7.1.1 SOIL MOISTURE STRESS
BENCHMARKING

## Slide 13
Indicator
Soil moisture stress: 120
National average: 110
Critical value (1) = 132
Optimal value (0) = 88
Normalised value: 0.73
Vulnerability Level: RATHER NEGATIVE
D7.1.1 SOIL MOISTURE STRESS
NORMALISATION

## Slide 14
D7.1.2 NUMBER OF ENDANGERED SPECIES
Description:
The number of species classified as endangered living in the area.
Objective:
To quantify biodiversity vulnerability at the local scale, to assess how drought contributes to species endangerment, to support environmental risk management by identifying ecological hotspots that need protection, and to integrate ecological indicators into drought risk assessment frameworks, linking environmental degradation to long-term sustainability.
Relevance:
Drought reduces surface water availability, making endangered species and species with specialised habitats needs particularly vulnerable. A high (or rising) number of endangered species indicates reduced ecosystem resilience.

## Slide 15
D7.1.2 NUMBER OF ENDANGERED SPECIES
Step 1: Find the number of endangered species living in the area in the local or national database
CALCULATION: STEP BY STEP

## Slide 16
Critical value (1) = 5 or more endangered species
Optimal value (0) = 1 endangered species
Range of values: lower is better (LIB)
D7.1.2 NUMBER OF ENDANGERED SPECIES
BENCHMARKING

## Slide 17
Indicator
Number of endangered species: 3
Normalised Value: 0,5
Vulnerability Level: NEUTRAL
D7.1.2 NUMBER OF ENDANGERED SPECIES
NORMALISATION

## Slide 18
D7.1.3 PERCENTAGE OF VULNERABLE HABITAT
Description:
Percentage of area covered by habitats that are at risk of drought. An expert estimates the risk of habitats.
Objective:
To quantify the spatial extent of habitats sensitive to drought stress, and to assess ecosystem exposure and vulnerability to reduced water availability.
Relevance:
Drought reduces soil moisture, groundwater levels and surface water flow, leading to habitat degradation or loss. A high percentage of vulnerable habitats indicates that local biodiversity and ecosystem services are at risk.

## Slide 19
D7.1.3 PERCENTAGE OF VULNERABLE HABITAT
Step 2: Based on your expert knowledge, estimate which of these habitats are at risk
CALCULATION: STEP BY STEP
Step 1: Use the local spatial plan in GIS to identify protected areas, natural habitats, etc.
Step 3: Calculate the area of habitats at risk
Step 4: Divide the area of habitats at risk by the total area of neighbourhood to get a percentage of habitats that are at risk

## Slide 20
Critical value (1) = 40% or more
Optimal value (0) = 0%
Range of values: lower is better (LIB)
D7.1.3 PERCENTAGE OF VULNERABLE HABITAT
BENCHMARKING

## Slide 21
Indicator
Percentage of vulnerable habitats: 15%
Normalized Value: 0,38
Vulnerability Level: RATHER POSITIVE
D7.1.3 PERCENTAGE OF VULNERABLE HABITAT
NORMALISATION

## Slide 22
D7.1.4 Percentage of protected areas
Description:
Percentage of area that is under Natura 2000 protection or similar.
Objective:
To quantify the extent of land under environmental protection and evaluate its role in reducing vulnerability, and to provide an indicator of ecological resilience and adaptive capacity within urban areas.
Relevance:
Protected areas often include water-rich or climate-buffering ecosystems that help retain water and maintain microclimates. They harbour biodiversity, ecological stability, and adaptive capacity. In the urban context, the presence of protected areas supports urban cooling, water retention and air quality regulation.

## Slide 23
D7.1.4 Percentage of protected areas
Step 1: Find the area of the Natura 2000 (or similar) protected area in the assessed neighbourhood
CALCULATION: STEP BY STEP
Step 2: Divide the Natura 2000 (or similar) area by the the total area of the neighbourhood to get the percentage

## Slide 24
Critical value (1) = 0%
Optimal value (0) = 40% or more
Range of values: higher is better (HIB)
D7.1.4 Percentage of protected areas
BENCHMARKING

## Slide 25
Indicator
Percentage of protected areas: 12%
Normalized Value: 0,7
Vulnerability Level: Rather negative
D7.1.4 Percentage of protected areas
NORMALISATION

## Slide 26
D7.1.5 PERCENTAGE OF WATERED URBAN GREEN SPACES
Description:
Percentage of urban green spaces that are regularly watered during the drought periods.
Objective:
To assess the sustainability and resilience of urban green infrastructure under drought conditions, to evaluate how much of a city’s green infrastructure depends on active watering and to what extent it is vulnerable to water scarcity.
Relevance:
Watered green spaces help maintain vegetation vitality, evapotranspiration cooling, and biodiversity habitats. Maintaining green areas mitigates the Urban Heat Island (UHI), and improves air quality.

## Slide 27
D7.1.5 PERCENTAGE OF WATERED URBAN GREEN SPACES
Step 1: Identify the area of all urban green spaces in neighbourhood
CALCULATION: STEP BY STEP
Step 2: Identify the area of urban green spaces that are frequently watered
Step 3: Divide the area of watered urban green spaces by the total area of urban green spaces to get the percentage
x 100

## Slide 28
Critical value (1) = 0%
Optimal value (0) = 100%
Range of values: higher is better (HIB)
D7.1.5 PERCENTAGE OF WATERED URBAN GREEN SPACES
BENCHMARKING

## Slide 29
Indicator
Percentage of watered urban green spaces: 40%
Normalised Value: 0,6
Vulnerability Level: Rather negative
D7.1.5 PERCENTAGE OF WATERED URBAN GREEN SPACES
NORMALISATION

## Slide 30: OVERALL VULNERABILITY
Criterion | Normalised value
Soil moisture stress | 0,73
Number of endangered species | 0,5
Percentage of vulnerable habitats | 0,38
Percentage of protected areas | 0,7
Percentage of watered urban green spaces | 0,6

## Slide 31: OVERALL VULNERABILITY
Criterion | Normalised value | Weight
Soil moisture stress | 0,73 | 0,25
Number of endangered species | 0,5 | 0,2
Percentage of vulnerable habitats | 0,38 | 0,15
Percentage od protected areas | 0,7 | 0,15
Percentage of watered urban green spaces | 0,6 | 0,25
TOTAL = 1 (100%)

## Slide 32
OVERALL VULNERABILITY (VULNERABILITY VALUE – VV)
Vulnerability Value (VV) = 0,5945
Vulnerability Level = RATHER NEGATIVE
VV = 0.73 x 0.25 + 0.5 x 0.2 + 0,38 x 0,15 + 0,7 x 0.15 + 0,6 x 0.25 = 0,5945
Weight
Normalised score
Criterion | Normalised value | Weight
Soil moisture stress | 0,73 | 0,25
Number of endangered species | 0,5 | 0,2
Percentage of vulnerable habitats | 0,38 | 0,15
Percentage od protected areas | 0,7 | 0,15
Percentage of watered urban green spaces | 0,6 | 0,25

## Slide 33
EXPOSURE OF INHABITANTS
AFTER ASSESSING VULNERABILITY, IT IS NECESSARY TO QUANTIFY TWO ADDITIONAL FACTORS TO DETERMINE THE LEVEL OF RISK:
-HAZARD
-EXPOSURE

## Slide 34
HAZARD LIKELIHOOD
Hazard Value (HV) = 0.6 (Occasional)
THIS INFORMATION IS PROVIDED BY SECAPs

## Slide 35
EXPOSED AREA
CODE | CRITERION | INDICATOR
D7.1-E1 | Exposed area | Area of urban green spaces

## Slide 36
EXPOSURE OF URBAN GREEN SPACES
Area of urban green space = 7
Critical value (1) = 10 km and more
Optimal value (0) = Less than 0,5 km
Normalised value (Exposure Value – EV) = 0,684
Exposure Level: MAJOR

## Slide 37
RISK ASSESSMENT
Hazard Value = 0,6
Exposure Value = 0,684
Vulnerability Value = 0,5945
WHV weight of HV
WEV weight of EV
WV weight of VV
0,25
0,25
RISK LEVEL = 0.62
RATHER NEGATIVE
Risk Category: Environment and biodiversity (D7)
Exposure: Damage risk for urban green spaces (D7.1)
0,5