## Slide 1
SuPeRBE Training Material
Climate change and built environment
Fundamentals of climate change
Level of competence: 2
Activity 3.2
SuPeRBE Project (CE0200768)
SuPeRBE Training Material
B10. Floods – Sanitary Systems
Level of competence: 1,2,3
B10.4 Drainage Systems
Macro Area of Expertise:
Area of Expertise:

## Slide 2
SuPeRBE Training Material
Climate change and built environment
Fundamentals of climate change
Level of competence: 2
Activity 3.2
SuPeRBE Project (CE0200768)
SuPeRBE Training Material
Level of competence: 1/2/3
Macro Area of Expertise 10:
Risk Assessment At Building Scale
Hazard: FLOODS (B)
Risk Category: Drainage Systems (B10.4)
Building Element: Sanitary Systems (B10)
Area of Expertise AD5.5:
ç
ç

## Slide 3: FLOODS
Floods happen when water overflows onto normally dry land, caused by heavy rain, river overflow, storm surges, or melting snow and ice. They are one of the most frequent and damaging climate-related hazards.
Why does it happen?
More extreme rainfall from climate change overwhelms rivers and drainage.
Sea-level rise increases coastal flooding and storm surge impacts.
Urbanization (paved surfaces, poor drainage) makes cities more flood-prone.
Deforestation and land use change reduce natural water absorption.
How frequent or severe?
Floods are happening more often and are becoming more intense, affecting millions of people annually. Some regions see Floods with 1-in-100 year intensity occurring far more frequently.
General Information

## Slide 4: FLOODS AND BUILDINGS
Exposure to floods can lead to:
Water infiltration, through façades, windows, basements, and ground level openings.
Deterioration of building loading capacity, through the water infiltration on structural system (walls, columns, piles, foundations)
Sewer backflow, re-entering buildings through floor drains.
Disruption of building operation, including temporary closure or limited access to some areas, and disruption in electricity and clean water services.
Damage to stored items, materials, appliances, personal belongings.
Temporary displacement of residents or workers
Impacts on public health due to derived issues, such as mold exposure, chronic respiratory conditions, and economic hardship that worsens health inequalities.

## Slide 5: RISK ASSESSMENT AT THE BUILDING SCALE
Hazard: Floods
Exposed Element: Drainage Systems
FLOODS
HAZARD
RISK CATEGORY
Damage risk for the Sanitary Systems
Drainage Systems
EXPOSED ELEMENT

## Slide 6: IMPACT CHAIN
INDICATOR
VALUE OF THE INDICATOR
CRITERION
ISSUE
RISK CATEGORY
FLOODS
RISK LEVEL
VULNERABILITY
Sensitivity
Level of
Adaptation
Damage risk for Sanitary System
EXPOSED ELEMENT
Drainage Systems

## Slide 7: VULNERABILITY CRITERIA AND INDICATORS
INDICATOR
VALUE OF THE INDICATOR
CRITERION
ISSUE
RISK CATEGORY
FLOODS
Drainage
Systems
RISK LEVEL
VULNERABILITY
Sensitivity
Level of
Adaptation
Damage risk for Sanitary Systems
EXPOSED ELEMENT
Code | Criterion | Indicator
B10.4.1 | Ground Level Hydrostatic Flood Vents | Size of ground level hydrostatic flood vents

## Slide 8
Description:
This criteria measures the size and number of ground-level hydrostatic flood vents designed to equalize water pressure and reduce structural damage during flooding.
Objective:
To assess whether the total size and number of ground-level hydrostatic flood vents are sufficient to equalize water pressure between the interior and exterior of enclosed spaces during flooding, thereby reducing structural stress and damage..
Relevance:
It is critical for building flood resilience, as properly sized hydrostatic flood vents help prevent wall failure, foundation damage, and costly structural repairs. By allowing controlled water entry and pressure equalization, the indicator supports safer building performance during flood events, reduces post-flood recovery needs, and ensures compliance with flood-resilient design standards and regulations..
B10.4.1. Ground Level Hydrostatic Flood Vents

## Slide 9
Indicator
Size of ground level hydrostatic flood vents
Type of value: High value is better
Units: m² of flood vent area per m² of enclosed area
Critical value (1) = 0
Optimal value (0) = 0.01 m² of flood vent opening per 1 m² of enclosed
B10.4.1. Ground Level Hydrostatic Flood Vents

## Slide 10
CALCULATION: STEP BY STEP
Step 1: Data Collection
Retrieve the design floorplans and drawings of the analysed building
Review design drawings and specifications to verify planned size and number of hydrostatic flood vents
Evaluate the total size (sum) of existing hydrostatic flood vents in the building of analysis
Compare this area value with the enclosed area of the building of analysis
Evaluate if the building meet resilience standards.
Step 2: Indicator Calculation
*Illustrative value for example purposes. Does not represent the current conditions of the case study
e.g. Veneria Reale, Piedmont, Italy
Primary school
Number of flood vents: 8
Total flood vent area: 0.9 m²
Building’s enclosed area: 110 m²
Compared to the proposed optimal value: 6 m
Indicator:
m² of flood vent per m² of building’s enclosed area
B10.4.1. Ground Level Hydrostatic Flood Vents

## Slide 11
CALCULATION: STEP BY STEP
Step 3: Normalize the result
The value is normalised applying the following formula (For Indicators where High Value is Better):
where:
Xi: value of the indicator
Xmax = optimal indicator’s value (corresponding to score 0)
Xmin = critical indicator’s value (corresponding to score 1)
Normalisation values | Description
0.1 | Optimal (No improvement necessary)
0.3 | Rather positive
0.5 | Neutral
0.7 | Rather negative
0.9 | Critical (Could lead to severe consequences)
Rather Positive - Optimal
e.g. Veneria Reale, Piedmont, Italy
Primary school
Period of study – January 2025
B10.4.1. Ground Level Hydrostatic Flood Vents