## Slide 1
SuPeRBE Training Material
Climate change and built environment
Fundamentals of climate change
Level of competence: 2
Activity 3.2
SuPeRBE Project (CE0200768)
SuPeRBE Training Material
B4. Floods - Facade
Level of competence: 1,2,3
B 4.2 Façade Openings
Macro Area of Expertise:
Area of Expertise:

## Slide 2
SuPeRBE Training Material
Climate change and built environment
Fundamentals of climate change
Level of competence: 2
Activity 3.2
SuPeRBE Project (CE0200768)
SuPeRBE Training Material
Level of competence: 1/2/3
Macro Area of Expertise 10:
Risk Assessment At Building Scale
Hazard: FLOODS (B)
Risk Category: Façade Openings (B4.2)
Building Element: FAÇADE (B4)
Area of Expertise AD5.5:
ç
ç

## Slide 3: FLOODS
Floods happen when water overflows onto normally dry land, caused by heavy rain, river overflow, storm surges, or melting snow and ice. They are one of the most frequent and damaging climate-related hazards.
Why does it happen?
More extreme rainfall from climate change overwhelms rivers and drainage.
Sea-level rise increases coastal flooding and storm surge impacts.
Urbanization (paved surfaces, poor drainage) makes cities more flood-prone.
Deforestation and land use change reduce natural water absorption.
How frequent or severe?
Floods are happening more often and are becoming more intense, affecting millions of people annually. Some regions see Floods with 1-in-100 year intensity occurring far more frequently.
General Information

## Slide 4: FLOODS AND BUILDINGS
Exposure to floods can lead to:
Water infiltration, through façades, windows, basements, and ground level openings.
Deterioration of building loading capacity, through the water infiltration on structural system (walls, columns, piles, foundations)
Sewer backflow, re-entering buildings through floor drains.
Disruption of building operation, including temporary closure or limited access to some areas, and disruption in electricity and clean water services.
Damage to stored items, materials, appliances, personal belongings.
Temporary displacement of residents or workers
Impacts on public health due to derived issues, such as mold exposure, chronic respiratory conditions, and economic hardship that worsens health inequalities.

## Slide 5: RISK ASSESSMENT FOR THE HEALTH OF INHABITANTS
Hazard: Floods
Exposed Element: Façade Openings
FLOODS
HAZARD
RISK CATEGORY
Damage risk for Façades
Façade Openings
EXPOSED ELEMENT

## Slide 6: IMPACT CHAIN
INDICATOR
VALUE OF THE INDICATOR
CRITERION
ISSUE
RISK CATEGORY
FLOODS
Façade
Openings
RISK LEVEL
VULNERABILITY
Sensitivity
Level of
Adaptation
Damage risk for Façades
EXPOSED ELEMENT

## Slide 7: VULNERABILITY CRITERIA AND INDICATORS
INDICATOR
VALUE OF THE INDICATOR
CRITERION
ISSUE
RISK CATEGORY
FLOODS
Façade
Openings
RISK LEVEL
VULNERABILITY
Sensitivity
Level of
Adaptation
Damage risk for Façades
EXPOSED ELEMENT
Code | Criterion | Indicator
B4.2.1 | Safe Windows and Shutters | Share of windows protected against hail.
B4.2.2 | Sealing Effectiveness | Share of openings with effective water/air infiltration protection.

## Slide 8
Description:
This indicator evaluates the percentage of windows equipped with hail-resistant glazing, shutters, or protective screens designed to withstand hail impact.
Objective:
To assess the building’s ability to reduce damage from hail events by evaluating the percentage of windows equipped with hail-resistant glazing, shutters, or protective screens designed to withstand hail impact without loss of performance or safety function.
Relevance:
Windows protected with hail-resistant materials or impact-tested shutters significantly decrease the risk of glass breakage, interior water infiltration, and costly post-event repairs during severe hailstorms. Ensuring robust window protection enhances occupant safety, safeguards interior assets, and preserves building functionality during extreme weather conditions. Increasing the share of protected windows strengthens overall building resilience, helps maintain property value, and supports climate-adaptive design in areas susceptible to frequent or intense hail events.
B4.2.1. Safe Windows and Shutters

## Slide 9
Indicator
Share of windows protected against hail
Type of value: High value is better
Units: %
Critical value (1) = 0%
Optimal value (0) = 100%
B4.2.1. Safe Windows and Shutters

## Slide 10
CALCULATION: STEP BY STEP
Step 1: Data Collection
Get the information about the number of protected windows of the investigated building during the year of assessment: hail-resistant or impact-resistant glazing, certified shutters or storm panels, protective external screens designed for hail impact. (Numerator)
Get the information about the total number of windows of the investigated building during the year of assessment (denominator).
Divide the number of protected windows by the total number of windows, and multiply by 100
B4.2.1. Safe Windows and Shutters
Step 2: Indicator Calculation
*Illustrative value for example purposes. Does not represent the current conditions of the case study
e.g. Veneria Reale, Piedmont, Italy
Primary school
Period of study – January 2025
Number of protected windows: 44
Total number of windows: 120
= 36,6% of protected windows in the building

## Slide 11
CALCULATION: STEP BY STEP
Step 3: Normalize the result
The value is normalised applying the following formula (For Indicators where High Value is Better):
where:
Xi: value of the indicator
Xmax = optimal indicator’s value (corresponding to score 0)
Xmin = critical indicator’s value (corresponding to score 1)
Normalisation values | Description
0.1 | Optimal (No improvement necessary)
0.3 | Rather positive
0.5 | Neutral
0.7 | Rather negative
0.9 | Critical (Could lead to severe consequences)
B4.2.1. Safe Windows and Shutters
Neutral
e.g. Veneria Reale, Piedmont, Italy
Primary school
Period of study – January 2025

## Slide 12
Description:
This indicator measures the percentage of building openings (e.g. windows, doors, vents) equipped with effective seals, gaskets, or membranes to prevent water and air infiltration.
Objective:
To assess how effectively the building envelope limits unwanted water and air infiltration through its openings. Its goal is to verify the presence of protective measures that reduce infiltration risks and support building resilience and energy efficiency.
Relevance:
Proper sealing of openings is essential for protecting the building against climate-related hazards such as wind-driven rain, humidity, and strong winds. Effective seals and gaskets help prevent moisture penetration, mold formation, and indoor air leakage, improving structural durability and indoor comfort. Furthermore, limiting infiltration reduces uncontrolled heat exchange, supporting thermal performance and decreasing energy demand for heating and cooling. This indicator directly contributes to safer, healthier, and more energy-efficient buildings, particularly in areas exposed to heavy rain, storms, or temperature fluctuations.
B4.2.2. Sealing Effectiveness

## Slide 13
Indicator
Share of openings with effective water/air infiltration protection
Type of value: High value is better
Units: %
Critical value (0) = 0%
Optimal value (1) = 100%
B4.2.2. Sealing Effectiveness

## Slide 14
CALCULATION: STEP BY STEP
*Illustrative value for example purposes. Does not represent the current
B4.2.2. Sealing Effectiveness
Step 1: Data Collection
Get the information about the number of protected openings of the investigated building during the year of assessment: effective seals, gaskets, or membranes to prevent water and air infiltration.. (Numerator)
Get the information about the total number of openings of the investigated building during the year of assessment (denominator).
Divide the number of protected openings by the total number of openigns, and multiply by 100
Step 2: Indicator Calculation
e.g. Veneria Reale, Piedmont, Italy
Primary school
Period of study – January 2025
Number of protected openings: 60
Total number of openings: 230
= 26% of protected openings in the building

## Slide 15
CALCULATION: STEP BY STEP
where:
Xi: value of the indicator
Xmax = optimal indicator’s value (corresponding to score 0)
Xmin = critical indicator’s value (corresponding to score 1)
Normalisation values | Description
0.1 | Optimal (No improvement necessary)
0.3 | Rather positive
0.5 | Neutral
0.7 | Rather negative
0.9 | Critical (Could lead to severe consequences)
B4.2.2. Sealing Effectiveness
Step 3: Normalize the result
The value is normalised applying the following formula (For Indicators where High Value is Better):
Rather negative
e.g. Veneria Reale, Piedmont, Italy
Primary school
Period of study – January 2025